## Slide 1: Philosoraptor
PHAT-TACO Experiment
Pressure Humidity And Temperature
Tests And Camera Observations
Hannah Gardiner, Bill Freeman, Randy Dupuis, Corey Myers, Andrea Spring
Skyhook
Team
Philosohook

## Slide 2: Preliminary Design Review (PDR)
Organization and Responsibilities
Goals and objectives
Science background
Technical background
Payload Design
Development plan

## Slide 3: Organization and Responsibilities
Member | Primary Responsibility | Secondary Responsibility
Hannah Gardiner | Project Management and editing | Testing and implementation
Bill Freeman | Software Design | Electrical Design and editing
Randy Dupuis | Electrical Design | Software Design
Andrea Spring | Mechanical Design | Project Management
Corey Myers | Testing and Implementation | Mechanical Design

## Slide 4: Mission Goal
To measure atmospheric conditions in order to study the layers of the atmosphere from liftoff to landing and study the surrounding environment of the payload in order to validate atmospheric conditions measured

## Slide 5: Objectives
The overall objective is to accurately measure and record internal and external temperature and humidity and external pressure on a balloon flight in order to study the atmosphere and take video of the flight.

## Slide 6: Science Objectives
Determine atmospheric layers flown through during flight
Characterize atmospheric conditions in layers
Determine effects of passing through clouds on temperature, pressure, and humidity
Identify the altitude range of cloud layers in order to estimate peaks in atmospheric turbulence and humidity
Determine balloon expansion as a function of altitude to approximate relative pressure

## Slide 7: Technical Objectives
Build a working payload that can withstand conditions of a balloon flight
Record temperature, pressure, and relative humidity up to 100,000 feet
Determine at what time and altitude the payload enters and exits clouds
Determine the radius of the balloon at several times, altitudes, and temperatures during flight
Achieve Pre-PDR, CDR, FRR, and final payload on time as specified by LaACES management

## Slide 8: Science background

## Slide 9: Science Background: Earth’s Atmosphere
Troposphere
  Clouds
Stratosphere
  Less humidity & lower pressure than the Troposphere
http://www.wyckoffschools.org/eisenhower/teachers/chen/atmosphere/earthatmosphere.htm

## Slide 10: US Model Atmosphere1 1976
“A hypothetical vertical distribution of atmospheric temperature, pressure, and density”
Can calculate properties of the atmosphere
  Pressure
  Temperature
  Density
1U.S. Standard Atmosphere, 1976, U.S. Government Printing Office, Washington, D.C., 1976.

## Slide 11: Temperature
Identify layers of atmosphere using temperature lapse rate
Chart: Temperature vs Altitude
Troposphere Tropopause Stratosphere
Theory
Oolman, Larry. "Atmospheric Soundings." Wyoming Weather Web. Web. 28 Nov. 2010. <http://weather.uwyo.edu/upperair/sounding.html>.

## Slide 12: Pressure
Chart: Pressure vs Altitude
Troposphere Tropopause Stratosphere
Oolman, Larry. "Atmospheric Soundings." Wyoming Weather Web. Web. 28 Nov. 2010. <http://weather.uwyo.edu/upperair/sounding.html>.
We shall compare measured pressure with expected pressure of the US Standard Atmosphere

## Slide 13: Balloon Radius
Kaymont 2000 gm sounding balloon
Ascent rate should be constant during flight
Has not been in previous flights

## Slide 14: Balloon Radius
R is the radius of the balloon in m
Dair is the density of air in kg/m3
g is gravitational acceleration in m/s2
C is the weight in newtons
k is a geometrical and substance factor in drag that is d’less
S is the vertical speed of the balloon in m/s
Summation of all forces on an object with constant velocity is zero:

## Slide 15: Balloon Radius vs. Altitude
Chart: Balloon Radius vs Altitude
| 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34
Radius no drag | 1.0355 | 1.1056 | 1.1841 | 1.2725 | 1.3728 | 1.4872 | 1.6337 | 1.8141 | 2.0142 | 2.2362 | 2.4825 | 2.7627 | 3.0716 | 3.4116 | 3.7855 | 4.1962 | 4.647 | 5.1624
Burst | 5.27
Radius w/ drag | 1.549 | 1.6767 | 1.8456 | 2.258 | 2.9 | 3.479 | 4.5912

## Slide 16: Placement of Camera
Placement of the camera is important
Too close and the apparent radius is not close to the actual radius (Camera A)
Too far and the radius is not easy to measure (Camera C)

## Slide 17: Technical background

## Slide 18: Temperature Sensors
Thermocouple
Operation: 0 to 1000°C
Cost: $75
Resistive Temperature Detector
Operation: -60 to 150°C
Cost: $1700
Thermistor
Operation: -80 to 150°C
Cost: $8.00
Diode
Operation: -65 to 200°C
Cost: $0.02
Required range: 30 to -70 ± 0.6 °C

## Slide 19: Pressure Sensors
Piezoelectric
Low cost, Small in Size, and High Repeatability
Produces Linear Output
Require a circuit with higher impedance to measure the voltage stored in the sensor
Voltage across the sensor can be lost before a measurement is taken
Piezoresistive
Low cost, Small in Size, and High Repeatability
Produces Linear Output
Better low frequency response than piezoelectric sensors
Required range: 1 to 0.008 ± 0.004 atm

## Slide 20: Humidity Sensors
Resistive
Output is related to relative humidity in an inverse exponential relationship
Operation: -40 to 100°C
Have protective coating to protect the circuitry
Capacitance changes linearly with relative humidity
Have built in circuitry to transform the output to a voltage
Operation:-40 to 85°C
Capacitive
Required range: 0 to 100 ± 0.5 % relative humidity

## Slide 21: Camera
CCD
Not as susceptible to noise
Can consume about 100x as much power as a CMOS
Higher quality, resolution, and sensitvity
CMOS
More susceptible to noise than CCD’s
Low power
Lower sensitivity due to light hitting transistors instead of photodiodes
Easier to mass produce and cost less

## Slide 22: Electronics design

## Slide 23: Control Electronics

## Slide 24: Possible Power Sources
Photovoltaic Panel
  Each cell produces about 0.5V
  Current depends on surface area and illumination
  Back up batteries required for cloud coverage
Thermoelectric Generator
  Require an active heat source
  More suited for deep space missions
Battery
  Light-weight, and inexpensive
  Variety of Voltages and Capacities available

## Slide 25: Power Budget
Component | Current (mA) | Voltage (V) | Power (mW) | Capacity (mA-hours)
Temperature Sensor | 1 | 12 | 12 | 4
Pressure Sensor | 2 | 12 | 24 | 8
Internal Humidity Sensor | 0.5 | 5 | 2.5 | 2
External Humidity Sensor | 0.5 | 5 | 2.5 | 2
Camera | 250 | 4.5 | 1125 | 1000
BalloonSat | 52 | 12 | 624 | 208
Total | 306 | 12 | 1790 | 1224

## Slide 26: Power Supplies
Supply | Current (mA) | Voltage (V) | Power (mW) | Capacity (mA-hours)
Power Supply 1 | 56 | 12 | 665 | 224
Power Supply 2 | 250 | 4.5 | 1125 | 1000
Total | 306 | 12 | 1790 | 1224
Supply | Current (mA) | Voltage (V) | Power (mW) | Capacity (mW-hours)
Power Supply1 | 56 | 1.5 | ~80 | 320
Power Supply 2 | 250 | 1.5 | ~375 | 1500
Power supply Requirements
Requirements for Each Battery in the Power Supply

## Slide 27: Software design

## Slide 28: Data Storage
Data Type | Minimum | Maximum | Precision | # steps | # bytes | Total Bytes
Pressure | 0.008 | 1 | 0.004 | 248 | 1 | 1
Temperature x2 | -70 | 30 | 0.5 | 240 | 1 | 2
Humidity x2 | 0 | 100 | 0.5 | 200 | 1 | 2
Timestamp (H,M,S) | 0 | 60 | 1 | 60 | 3 | 3
1 Data point every 6 seconds (10/min)
100 minutes ascent – 1000 data points
Storage needed – 8000 bytes
EEPROM storage – 8191 bytes
Total time to take data – 102 minutes
Total time to take data – 408 minutes
Secure Digital: 2$/GB
Flash memory: 2.5$/GB

## Slide 29: During Flight Flowchart
Must take data every six seconds
Stores data in raw ADC counts
Can’t run out of memory before ascent is over
Can’t overwrite data if the power restarts

## Slide 30: Pre Flight Flowchart
Must be able to calibrate Real Time Clock (RTC)
LaACES Management will provide a flight profile of altitude vs time
This program sets the time and allows for the During Flight program to start at the correct location

## Slide 31: Post Flight Flowchart
Must be able to read out all data to debug screen
Excel data sheet will contain conversions from ADC counts to atmospheres, kelvin, and % humidity
Excel sheet will also convert timestamps into altitude

## Slide 32: Post Flight Data Processing
EEPROM readout data
  Timestamp -> altitude
  ADC counts -> pressure, temperature, humidity
Video data
  Video timestamp -> altitude
  Video -> size of balloon (pixels -> cm)
  Video -> cloud types
  Video -> payload passing through cloud

## Slide 33: Mechanical design

## Slide 34: Thermal Design
Temperature Range: -70oC to 25oC
Construction Material: Insulating foam with a very low thermal conductivity
Heat produced by electronics
Component | Lowest Temp. (oC) | Highest Temp. (oC)
Electronics | -40 | 85
Pressure Sensor | -20 | 85
Humidity Sensor | -40 | 85
Temp Sensor | -65 | 200
Camera | -20 | 100
Batteries | -40 | 60

## Slide 35: Payload Design
External
Hexagonal
  9.5 cm sides
  21 cm high; 23 cm including the bottom
2 holes in the lid
  Temperature and Humidity Sensors
  Camera
Internal
Balsa wood 7.5 cm wide and 21 cm
  Hold components
  Increase stability
Camera against opposite wall

## Slide 36: External Design - Drawings
Top
Front
Side

## Slide 37: Development

## Slide 38: Timeline and Milestones

## Slide 39: Payload Development Plan
The next step in our project
We must know the specifications for our project in order to move on to the CDR stage
Sensors and the camera type will be finalized for prototyping
Circuitry will be prototyped on a solderless breadboard
The payload box will also be prototyped

## Slide 40: What is next
FRR
  Final payload box is made
  Electrical components put together
  Software is finalized
Launch trip
  FRR Defense
  Balloon Flight and data acquisition
  Science presentation

## Slide 41: Questions?