## Slide 1
PHAT-TACO Experiment
Pressure Humidity And Temperature
Tests And Camera Observations
Hannah Gardiner, Bill Freeman, Randy Dupuis, Corey Myers, Andrea Spring
Team
Philosohook

## Slide 2: Critical Design Review
Goals and objectives
Science background
Payload Design
Mechanical Design
Electronics Design
Software Design
Flight Operations
Budgeting and Development

## Slide 3: Mission Goal
To study the layers of the atmosphere using an instrumented sounding balloon flown in East Texas during May and to analyze the balloon and the environment surrounding the payload in order to study the relationship between the temperature and humidity profiles acquired during flight.

## Slide 4: Objective
The overall objective is to measure and record humidity, pressure, and internal and external temperature on a sounding balloon flight while taking video of the flight.

## Slide 5: Science background

## Slide 6: Science Background: Earth’s Atmosphere
Troposphere
  Clouds
Stratosphere
  Less humidity & lower pressure than the Troposphere
http://www.wyckoffschools.org/eisenhower/teachers/chen/atmosphere/earthatmosphere.htm

## Slide 7: US Model Atmosphere1 1976
“A hypothetical vertical distribution of atmospheric temperature, pressure, and density”
Can calculate properties of the atmosphere
  Pressure
  Temperature
  Density
1U.S. Standard Atmosphere, 1976, U.S. Government Printing Office, Washington, D.C., 1976.

## Slide 8: Balloon Radius
Kaymont 3000 gm sounding balloon
Ascent rate should be constant during flight
Has not been in previous flights

## Slide 9: System design

## Slide 12: Mechanical design

## Slide 13: Thermal Design
Temperature Range: -80oC to 30oC
Construction Material: Insulating foam with a low thermal conductivity
Heat produced by electronics
-3.9oC
Component | Lowest Temp. (oC) | Highest Temp. (oC)
Electronics | -40 | 85
Pressure Sensor | -20 | 85
Humidity Sensor | -40 | 85
Temp Sensor | -65 | 200
Camera | -40 | 100
Batteries | -40 | 60

## Slide 14: Payload Design
External
Hexagonal
  9.5 cm sides
  10 cm high; 14 cm including the bottom
2 holes in the lid
  Temperature and Humidity Sensors
  Camera
Internal
BalloonSat, sensors and conditioning will be on the bottom
Camera will be in a cut out in the top
Camera will be secured by duct tape and an optional basswood shelf

## Slide 15: Mechanical Drawings
Front
Side
Top
Axonometric

## Slide 16: Weight Budget
Component | Weight (g) | Uncertainty (+/-g) | Measured or estimated
BalloonSat | 65 | 2 | Measured
Power Supply 1 | 65 | 2 | Measured
Power Supply 2 | 80 | 2 | Measured
Signal Conditioning Board and sensors | 65 | 5 | Estimated*
Foam Structure | 50 | 15 | Measured
Camera | 95 | 5 | Measured
Total | 420 | 28 | 

## Slide 17: Electronics design

## Slide 18: Temperature Sensor Interface

## Slide 19: Pressure Sensor Interface

## Slide 20: Humidity Sensor Interface

## Slide 21: Camera Interface

## Slide 22: Power

## Slide 23: Power Budget
Component | Current (mA) | Voltage (V) | Power (mW) | Capacity (mA-hours)
Temperature Sensor | 1.2 | 12 | 14.4 | 4.8
Pressure Sensor | 2.1 | 12 | 25.2 | 8.4
Humidity | .5 | 12 | 6 | 2
Balloon Sat | 52 | 12 | 624 | 208
Camera | 220 | 7 | 1540 | 880
Power Supply 1 | 55.8 | 12 | 669.6 | 223.2
Power Supply 2 | 220 | 7 | 1540 | 880

## Slide 24: Battery Selection
Power Supply 1 | 58 | 12 | 680.6 | 232
Power Supply 2 | 220 | 7 | 1540 | 880
Component | Current (mA) | Voltage (V) | Power (mW) | Capacity (mA-hours)

## Slide 25: Software design

## Slide 26: Software Background
Basic stamp controls everything
Measure and record temperature, pressure, and humidity every six seconds
Check to see if the camera is recording
Stop, then restart the video every 10 minutes
Save “camera status byte” to EEPROM

## Slide 27: Pre Flight Flowchart
Must be able to calibrate Real Time Clock (RTC)
LaACES Management will provide a flight profile of altitude vs time
This program sets the time and allows for the During Flight program to start at the correct location
First two bytes on the EEPROM store the location of the last saved data point

## Slide 28: During Flight
Controls all aspects of the payload
Takes T,P,H data every 6 sec
Also checks if the camera is still recording

## Slide 29: During Flight Subroutines
Makes sure the camera is recording
If camera is not recording, this subroutine tries to start recording again
Status nibble set so we know what is happening to the camera

## Slide 30
During Flight Subroutines
If the camera is recording, stop recording
Set status nibble according to how the subroutine ends

## Slide 31: Post Flight Flowchart
Must be able to read out all data to debug screen
Excel data sheet will contain conversions from ADC counts to atmospheres, kelvin, and % humidity
Excel sheet will also convert timestamps into altitude

## Slide 32: Post flight Balloon Radius Calculator
Doesn’t need entire balloon to calculate radius
Works similar to most “fitting” programs
Better than only using two points

## Slide 33: Post Flight Data Processing
EEPROM readout data
  Timestamp -> altitude
  ADC counts -> pressure, temperature, humidity
Video data
  Video time + EEPROM information -> altitude
  Video -> size of balloon (pixels -> cm)
  Video -> payload passing through cloud

## Slide 34: Magical Post-Flight Excel Sheet
Data will be in comma delimited text file after downloading with Term232
Equations will already be programmed into sheet
Also calculates uncertianties
Will convert EEPROM timestamp into guzik-friendly format

## Slide 35: Flight Operations: Testing

## Slide 36: Shock Test
With the system powered up and the lid taped down, the payload will be dropped from a height of 5 ft.
After the drop, the lid will be removed and all components checked and any shifting noted.
Data must verify that the force involved in the test did not disrupt the data collection process.

## Slide 37: Vacuum Test
The powered up payload will be placed in the vacuum chamber.
The vacuum will be turned on to decrease the pressure for one hour.
Data must be verified that it was recorded accurately throughout the length of the test.

## Slide 38: Thermal Test
The powered up payload will be placed first at room temperature for 15 minutes.
Refrigerator for 45 minutes.
A dry ice cooled environment, approximately -78°C, for an hour.
Refrigerator for 45 minutes.
Room temperature for 15 minutes.
Data must be verified that it was recorded accurately throughout the length of the test.

## Slide 39: Flight Operations: Calibrations

## Slide 40: Temperature Calibration
Use HOBO to measure temperatures at various locations alongside the sensor.
The sensor and Hobo will measure
  Room temperature.
  Refrigerator.
  Icebox filled with dry ice.
  Outside the physics building.
Each temperature placement will be carried out for 10-15 minutes.
The voltage output data from our sensor will be compared to the data from the HOBO

## Slide 41: Humidity Calibration
The HOBO sensor will be used to accurately measure the humidity in various conditions
Both placed in sealable container inside saturated environment at 0˚C
Seal container
Transport container to varying temperatures
The voltage output data from our sensor will be compared to the data from the HOBO

## Slide 42: Humidity Calibration
Chart: Humidity vs Temperature
| 0 | 5 | 10 | 15 | 20 | 25 | 30
Relative Humidity | 1 | 0.70103 | 0.49788 | 0.35855 | 0.26142 | 0.19486 | 0.14405
http://www.engineeringtoolbox.com/humidity-ratio-air-d_686.html

## Slide 43: Pressure Calibration
We will adjust the variable resistor on the payload to set ground-level pressure
The payload will be placed in the vacuum chamber
We will stop the vacuum chamber and allow the pressure sensor to take several measurements at that pressure and record the pressure indicated by the vacuum chamber pressure gauge.
A line of best fit will be created for the pressure sensor’s output voltage versus absolute pressure.

## Slide 44: Camera Calibration
First we will start the camera to make sure it is operating properly.
A fellow teammate holding a ruler will stand at a prescribed distance away from the camera.
Video will be taken for about 1-2 minutes in order to collect data.
After data collection is complete, the pixels of the camera images will be used to determine the angular resolution of the pixels.

## Slide 45: Pre-Launch Checklist
Event | Time needed
Verify that all components are ready for flight and operational. | 10 minutes
Load the correct pre-flight software and during flight software. | 5 minutes
Put in the appropriate fresh batteries for each of the power sources and make sure each power source is connected to its appropriate components. | 2 minutes
Place components in payload and tape the lid shut and check to make sure camera is facing up and through the hole in the lid. | 1 minute
Attach the payload to the launch vehicle and check to make sure it is secure. | 10 minutes
Measure distance from Balloon to payload. | 2 minutes
Total Time | 30 minutes

## Slide 46: Payload Recovery
Telemetry will be tracked by GPS satellite signals via additional payloads on balloon vehicle
Sounding beacon
Colorful parachute

## Slide 47: Budgeting and Development

## Slide 48: Budget
Component | Price
Temperature Sensor | $0.02
Pressure Sensor | $40
Humidity Sensor | $14.11
Camera | $40
32 GigaByte SD Card | $64
Expanded EEPROM | $1.50
Batteries | $12
Single OpAmp Integrated Circuit | $2.25
BalloonSat | --
Miscellaneous parts and contingency | $170
Total Expected Expenditure: | $343.88

## Slide 49: Timeline

## Slide 50: What is next
Integration phase
  Components are created
  Connect together
  Test
  Debug
Systems testing phase
  Calibrate systems
  Thermal, shock, and vacuum tests
FRR Defense
Flight
Analysis and Science Presentation

## Slide 51: Questions
?