## Slide 1
PHAT-TACO Experiment
Pressure Humidity And Temperature
Tests And Camera Observations
Hannah Gardiner, Bill Freeman, Randy Dupuis, Corey Myers, Andrea Spring
Team
Philosohook

## Slide 2: Flight Readiness Review
Goals and objectives
Science background
Payload Design
Mechanical Design
Electronics Design
Software Design
Flight Operations

## Slide 3: Mission Goal
To study the layers of the atmosphere using an instrumented sounding balloon flown in East Texas during May and to analyze the balloon and the environment surrounding the payload in order to study the relationship between the temperature and humidity profiles acquired during flight.

## Slide 4: Objective
The overall objective is to measure and record humidity, pressure, and internal and external temperature on a sounding balloon flight while taking video of the flight.

## Slide 5: Science background

## Slide 6: Science Background: Earth’s Atmosphere
Troposphere
  Clouds
Stratosphere
  Less humidity & lower pressure than the Troposphere
http://www.wyckoffschools.org/eisenhower/teachers/chen/atmosphere/earthatmosphere.htm

## Slide 7: US Model Atmosphere1 1976
“A hypothetical vertical distribution of atmospheric temperature, pressure, and density”
Can calculate properties of the atmosphere
  Pressure
  Temperature
  Density
1U.S. Standard Atmosphere, 1976, U.S. Government Printing Office, Washington, D.C., 1976.
Notes: Possible deletion

## Slide 8: Balloon Radius
Kaymont 3000 gm sounding balloon
Ascent rate should be constant during flight
Has not been in previous flights

## Slide 9: System design

## Slide 12: Mechanical design

## Slide 13: Thermal Design
Temperature Range: -80oC to 30oC
Construction Material: Insulating foam with a low thermal conductivity
Heat produced by electronics
15.8oC
Component | Lowest Temp. (oC) | Highest Temp. (oC)
Electronics | -40 | 85
Pressure Sensor | -20 | 85
Humidity Sensor | -40 | 85
Temp Sensor | -65 | 200
Camera | -40 | 100
Batteries | -40 | 60

## Slide 14: Payload Design
External
Hexagonal
  10 cm sides
  14 cm high; 17.5 cm including the bottom
1 hole in the lid for the camera
Internal
A 14 cm x 15.5 cm insert will hold all components
Batteries and camera on one side
BalloonSat and Conditioning on the other
Secured by Velcro

## Slide 15: Mechanical Drawings - External
Top
Front

## Slide 16: Mechanical Design - Internal

## Slide 17: Mechanical Design - Internal

## Slide 18: Mass Budget
Component | Mass (g) | Uncertainty (+/-g)
BalloonSat | 66.3 | .05
Power Supply 1 | 71.8 | .05
Power Supply 2 | 63.7 | .05
Signal Conditioning Board and sensors | 101.5 | .05
Foam Structure | 99.6 | .05
Camera | 97.8 | .05
Total | 500.7 | .12

## Slide 19: Electronics design

## Slide 20: Temperature Sensor Interface

## Slide 21: Pressure Sensor Interface

## Slide 22: Humidity Sensor Interface

## Slide 23: Camera Interface

## Slide 24: Power

## Slide 25: Power Budget
Component | Current (mA) | Voltage (V) | Power (mW) | Capacity (mA-hours)
Temperature Sensor | 1.2 | 12 | 14.4 | 4.8
Pressure Sensor | 2.1 | 12 | 25.2 | 8.4
Humidity | .5 | 12 | 6 | 2
Balloon Sat | 52 | 12 | 624 | 208
Camera | 220 | 6 | 1320 | 880
Power Supply 1 | 55.8 | 12 | 669.6 | 223.2
Power Supply 2 | 220 | 6 | 1540 | 880

## Slide 26: Software design

## Slide 27: Software Background
Basic stamp controls everything
Measure and record temperature, pressure, and humidity every six seconds
Check to see if the camera is recording
Stop, then restart the video every 10 minutes
Save “camera status byte” to EEPROM

## Slide 28: Pre Flight Flowchart
Must be able to calibrate Real Time Clock (RTC)
LaACES Management will provide a flight profile of altitude vs time
First two bytes on the EEPROM store the location of the last saved data point

## Slide 29: During Flight
Controls all aspects of the payload
Takes T,P,H data every 6 sec
Also checks if the camera is still recording

## Slide 30: Post Flight Flowchart
Must be able to read out all data to debug screen
Excel data sheet will contain conversions from ADC counts to atmospheres, kelvin, and % humidity
Excel sheet will also convert timestamps into altitude

## Slide 31: Post flight Balloon Radius Calculator
Doesn’t need entire balloon to calculate radius
Works similar to most “fitting” programs
Better than only using two points

## Slide 32: Flight Operations: Testing

## Slide 33: Thermal Test
Chart: Thermal Test: Internal and External Temperature

## Slide 34: Vacuum Test

## Slide 35: Shock Test
Chart: Shock Test
| -30 | -24 | -18 | -12 | -6 | 0 | 6 | 12 | 18 | 24 | 30
intemp | 252 | 252 | 252 | 252 | 252 | 252 | 252 | 252 | 252 | 252 | 252
outtemp | 8 | 8 | 7 | 7 | 8 | 7 | 8 | 8 | 8 | 8 | 8
pres | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255
humidity | 95 | 94 | 92 | 92 | 92 | 93 | 95 | 96 | 96 | 94 | 95
cam | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 36: Flight Operations: Calibrations

## Slide 37: Temperature Calibration
External temperature sensor:
Temperature(C°) = -.4439(ADC Count) + 28.3
Error: ((.013151*ADC Count)^2+(.917709)^2)^.5 C°

## Slide 38: Temperature Calibration
Internal temperature sensor:
Temperature(C°) = 1.5648(ADC Count) - 364.2
Error: 2.07 C° (error variation because of ADC Counts is very small)

## Slide 39: Pressure Calibration
Pressure
Counts
Pressure Sensor:
Pressure(Atm)=.0039464(ADC counts)-.002953703
Error=((1.98378e-5*ADC counts)^2+(.002055339)^2)^.5 Atm

## Slide 40: Humidity Calibration
Humidity
Counts
Humidity Sensor:
RH(%)= 0.4003(ADC count) – .1047
Error: ((0.01453*ADC count)^2+(2.706038)^2)^.5%

## Slide 41: Pre-Launch Checklist
Event | Time needed | T- minus to launch
Verify that all components are ready for flight and operational. | 10 minutes | 2 days
Run pre-flight software | 25 minutes | 12 hours
Load during flight software | 1 minute | 11.5 hours
Put in the appropriate fresh batteries for each of the power sources and make sure each power source is connected to its appropriate components. | 2 minutes | 1 hour
Place components in payload and tape the lid shut and check to make sure camera is facing up and through the hole in the lid. | 1 minute | 1 hour
Attach the payload to the launch vehicle and check to make sure it is secure. | 10 minutes | 45 minutes
Take picture from a distance in order to calculate distance from payload to balloon. | 2 minute | 5 minutes
Total Time | 51 minutes | 

## Slide 42: What is next
Flight
Analysis of data
Science Presentation

## Slide 43: Questions
?